## Slide 1: Co-existence of a GUI and the main terminal: How was it achieved with the DFTVisualizer GUI with TCL/TK as the implementation language and the related changes?
By
Tarun Kumar Goyal
Roshni Lalwani
Mentor Graphics Noida

## Slide 2: Agenda
GUI and non-GUI coexistence: a brief
How was it accomplished in DFTVisualizer (DFTV): the details
  Invocation time and system settings including the external packages to make main shell TCL-ish
  Client (DFTVisualizer) side changes for handshaking with main shell
  Related changes to exploit the capability in DFTVisualizer making transcript as clone of main shell

## Slide 3: Why GUI and non-GUI should co-exist?
GUI more becoming the de-facto debugging places with main shell the main driver necessitating the co-existence.
GUI becomes really handy when a user has limited exposure to a particular design methodology
A console in GUI helps a user execute scripts/commands from within the GUI itself along with several other advantages such as hyperlinking etc. that a console can offer to add value to the design process of a fabless design engineer.
Main shell
DFTVisualizer

## Slide 4: Core settings for main-shell and DFTVisualizer co-existence
Invocation time initializations to make sure that TCL/TK packages are sourced properly along with setting things for “eltclsh” package to make main shell TCL-ish
Tclappinit() { // Calculate platform specific info and set it properly to invoke the GUI tcl_lib_relative = gen_lib_relative + "/tcl" + TCL_VERSION; tck_lib_relative = gen_lib_relative + "/tk" + TK_VERSION; // eltclsh make the main console tclish in nature and can accept all tcl tk commands eltclsh_lib_relative = gen_lib_relative + "/eltclsh-1.11.1 // initialise the master interpreter on which the main shell/console shall be registered tclInterpreters_[MasterInterpreter] = Tcl_CreateInterp(); // Override default Tcl pre init script because of the bug during creation of slave interp // It will also set tcl_library and tk_library appropriately setTclPreInitScript(tclpath, tkpath); // initialise the master interpreter Tcl_Init(masterInterp())

## Slide 5: Core settings Contd……
……… // initialise the slave interpreters one of which will have the DFTVisualizer GUI // Very important to note here that GUI gets to the slave interp for (unsigned i(0); i < TclInterpreterTag_END; ++i) { TclInterpreterTag tag(static_cast<TclInterpreterTag>(i)); if (MasterInterpreter == tag) { continue; } if ((DftvInterpreter == tag) && !createDftvInterp()) { continue; } tclInterpreters_[tag] = Tcl_CreateSlave(masterInterp(), nameOf(tag).c_str(), 0); } // initialise eltclsh which forms the backbone for TCLishing of the main console and set it up properly for (unsigned i(0); i < TclInterpreterTag_END; ++i) { TclInterpreterTag tag(static_cast<TclInterpreterTag>(i)); Tcl_Interp* interp(getTclInterp(tag)); if (!interp) { continue; } Tcl_SetVar(interp, "eltclsh_library", eltclshpath.c_str(), TCL_GLOBAL_ONLY); } // Setup all the interpreters with proper TCL variable values for (unsigned i(0); i < TclInterpreterTag_END; ++i) { Tcl_ListObjAppendElement(interp, auto_path, Tcl_NewStringObj(genlibpath.c_str(), -1)); Tcl_ListObjAppendElement(interp, auto_path, Tcl_NewStringObj(tclpath.c_str(), -1)); Tcl_ListObjAppendElement(interp, auto_path, Tcl_NewStringObj(tkpath.c_str(), -1)); ……………… Tcl_CreateCommand(interp, "TclAppPrompt", TclAppPrompt, (ClientData)NULL, (Tcl_CmdDeleteProc *)NULL); Tcl_Eval (interp, "set tcl_prompt1 TclAppPrompt" ); ………………. }

## Slide 6: Concluding core settings at startup …
/* Create a body for unknown and Call Tessent_Unknown from unknown. * The reason for this indirection is because some packages (e.g. itcl) use [info body unknown] during runtime. *Using UPLEVEL to 1: Make the additional indirection transparent to our unknown handler. * 2: Explode the var arg list (args) back to individual arguments before calling our unknown handler. */ // string TessentUnknownBody = "if {[info command ::Tessent_Unknown] != \"\"} {return [uplevel Tessent_Unknown $args]}"; string TessentUnknownBody = "if {[info command ::Tessent_Unknown] != \"\"} {\n"; TessentUnknownBody += " set newcmd [linsert $args 0 ::Tessent_Unknown]\n"; TessentUnknownBody += " uplevel 1 [list ::catch $newcmd ::tcl::UnknownResult ::tcl::UnknownOptions]\n"; …………………. // Create a new Tcl command called Tessent_Unknown and bind it to our unknown handler Tcl_CreateObjCommand( interp, "Tessent_Unknown", UnknownCmd, (ClientData)NULL, NULL ); Tcl_Eval(interp, unknownDef.c_str()); } }

## Slide 7: Interaction of DFTV GUI with the “core” after settings are done
Interaction happens through a set of predefined “core” registered commands for the GUI actions.
//call the C registered TCL command from tcl/tk c_DftKernelExecute “$command” // since proper escaping / issuing modern commands, on DFTVis Transcript is the onus of the user. string tclcmd(data);; if(!isCallFromTranscript()) { // first convert the command into 3_2_1 syntax tclcmd = ConvertToModernCommand(tclcmd); // special handling in case there are escape characters in the command tclcmd = ComTcl_EscapeForTcl(tclcmd, false, true); } // execute the command in the core command handler // DFTApp is the class that manages the command execution of the main shell DftApp::get().execCommand(data, msg, !isCallFromTranscript(), !isCallFromTranscript())))

## Slide 8: Making the main-shell TCL-ish in nature
We have adopted “eltclsh” (editline tcl shell) to make our main shell interactive in nature
  provides command line editing, history browsing as well as variables and command completion
  open-source software released under a BSD license
// Setting the variables for eltclsh and calling the initialize function of
// eltclsh which runs a while(1) loop for “smart” (such as editing,
// history etc.) input options on main shell
Tcl_SetVar(interp, "eltclsh_library", eltclshpath.c_str(), TCL_GLOBAL_ONLY)
“eltclsh” was customized for our own consumption especially the handshaking beween tool command dictionary and completion (next slide has details)
  Tcl_CreateCommand registered commands on a given TCL interpreter are visible to the “eltclsh” as well and is used while performing various key functions such as TAB completion, arrows keys, history etc.

## Slide 9: Custom command completion for eltclsh to work with our tools
// Our Custom command-line completion procedure that operate on a 3_2_1 commands unsigned char elTclNewCompletion(EditLine *el, int ch) { // get context on which the commands registered will show up and matched against el_get(el, EL_CLIENTDATA, &iinfo); linfo = el_line(el); // compute current command line: it is the concatenation of the current command // (any incomplete lines entered so far) plus the current editline buffer cmd[1] = Tcl_DuplicateObj(iinfo->command); // call the procedure that generates completion matches sprintf(buffer, "%d", iinfo->windowSize); cmd[0] = Tcl_NewStringObj("el::Get_Completion_Data", -1); // handles different cases based on number of matches // no match or unique match, process accordingly if (count == 0) return CC_ERROR; if (count == 3) { el_insertstr(el, Tcl_GetStringFromObj(matchList[1], NULL)); return CC_REFRESH;} // Multiple Match if (count == 4) { Tcl_ListObjGetElements(iinfo->currentInterp, matchList[0], &count, &matches); // ask user if matches exceed threshold // process the information based on “y”/”n” received by the user // restore back the text user typed before pressing TAB } } // put the results on the standard output fputs(Tcl_GetStringFromObj(matchList[3], NULL), stdout); } }

## Slide 10: Using the “eltclsh” operations at client end to perform smart functions
Case 1: In order to disable it for some commands/commands not following a given syntax: e.g. we want eltclsh to honor only 3_2_1 and not support “3 2 1” syntax we disabled it for latter case.
/* Turn Off TAB Auto-completion for LEGACY “3 2 1“commands */
if (GlobalCommandDictSingleton::getCommandDict().commandStyle() ==
CommandDict::LEGACY)
int status = Tcl_Eval(interp, "::el::Set_Auto_Completion 0");
Case 2: Retrieving the history of commands
int status = Tcl_Eval(currentInterp(), "el::get_history_data history_line");
Case3: Adding the command to the eltclsh history
string command = string("el::add_history_data ") + string("{") + line + string("}");
Case 4: Showing the completion matches on pressing the tab
cmd[0] = Tcl_NewStringObj("el::Get_Completion_Data", -1);
cmd[1] = Tcl_NewStringObj(partialWord.c_str(), -1); // such as “se” for “set_system_mode”
Tcl_ListObjGetElements(currentInterp(), cmd[0], &count, &matchList);
Tcl_GetIntFromObj(currentInterp(), matchList, &start);

## Slide 11: DFTVisualizer GUI transcript : mirror image of main shell
To mirror the GUI transcript to main shell
  All the messaging , commands and prompts shown in main shell are shown in transcript as well and vice versa.
  Tab , history and up/down arrow keys support done same as that of main shell.
To mirror any command entered on main shell
  The command entered, command result and prompt displayed on shell
    Also displayed in GUI transcript .
  For that three callbacks are set.
    PrologueCallback
      Called before the command execution.
      Displays command entered on the shell.
    CommandResultRedirectCallback
      Called when the command is executed.
      Command results are stored in internal buffer.
    EpilogueCallBack(epilogue_callback)
      Called after command execution.
      Display the results from internal buffer into console
      Displays command prompt in console (same as that of Shell)

## Slide 12: Pseudo code for mirroring command entered on shell
// if the command is issued on Shell then mirroring the same to console
// this callback is get called before the command execution
bool prologue_callback string& commandString ) {
showCommandInConsole(command.c_str());
}
// this callback is gets called when the command is executed
void command_result_redirect_callback ( const char* result ) {
// add commands result into to the internal buffer
appendCommandResultToBuffer(text);
}
bool epilogue_callBack (const string& command, int status) {
display_textFromBuffer_in_console(); // text of internal buffer is displayed in console
redirect_prompt_from_shell_to_console(); // display the prompt displayed in console
}

## Slide 13: Mirroring of command entered on GUI transcript
To mirror any command entered on GUI transcript
  Done similar to mirroring of command entered on main shell.
// this callback is get called before the command execution
bool prologue_callback string& commandString ) {
show_command_in_shell(command.c_str());
}
// this callback gets called when the command is executed
void command_result_redirect_callback ( const char* result ) {
display_command_result_in_shell(text);
}
bool epilogue_callBack (const string& command, int status) {
redirect_prompt_from_console_to_shell(); // display the prompt in shell
}

## Slide 14: Mirroring of Tab Support in console
The main shell runs on
  Master interpreter.
GUI transcript runs on
  Slave interpreter.
Results from master interpreter are stored in string.
The same are displayed in GUI transcript.
PSEUDO-CODE
// Tcl method called when tab key is
//pressed after entering some text on console
Proc tabExpandMethod {tab_str} {
  set _tabResultString [Get_Tab_Completion_Data_From_Shell $tab_str
  foreach tabStr $tabResultString {
  // display each tabStr in proper column format.
  }
}
int Get_Tab_Completion_Data_From_Shell { } {
elTclParseCommand()
// format the results in proper columns
formatCommandResults and return
}

## Slide 15
THANK YOU